## Slide 1: Image Filtering

## Slide 2: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 3: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 4: Motivation: Noise reduction
Given a camera and a still scene, how can you reduce noise?
Take lots of images and average them!
What’s the next best thing?
Source: S. Seitz
Notes: Answer: take lots of images, average them

## Slide 5: Moving average
Let’s replace each pixel with a weighted average of its neighborhood
The weights are called the filter kernel
What are the weights for the average of a 3x3 neighborhood?
1
1
1
1
1
1
1
1
1
“box filter”
Source: D. Lowe

## Slide 6: Defining Convolution
f
Let f be the image and g be the kernel. The output of convolving f with g is denoted f * g.
Source: F. Durand
Convention: kernel is “flipped”
MATLAB: conv2 (also imfilter)

## Slide 7: Key properties
Linearity: filter(f1 + f2 ) = filter(f1) + filter(f2)
Shift invariance: same behavior regardless of pixel location: filter(shift(f)) = shift(filter(f))
Theoretical result: any linear shift-invariant operator can be represented as a convolution

## Slide 8: Properties in more detail
Commutative: a * b = b * a
  Conceptually no difference between filter and signal
Associative: a * (b * c) = (a * b) * c
  Often apply several filters one after another: (((a * b1) * b2) * b3)
  This is equivalent to applying one filter: a * (b1 * b2 * b3)
Distributes over addition: a * (b + c) = (a * b) + (a * c)
Scalars factor out: ka * b = a * kb = k (a * b)
Identity: unit impulse e = […, 0, 0, 1, 0, 0, …], a * e = a

## Slide 9: Annoying details
What about near the edge?
  the filter window falls off the edge of the image
  need to extrapolate
  methods:
    clip filter (black)
    wrap around
    copy edge
    reflect across edge
Source: S. Marschner

## Slide 10: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
?
Source: D. Lowe

## Slide 11: Practice with linear filters
0
0
0
0
1
0
0
0
0
Original
Filtered
(no change)
Source: D. Lowe

## Slide 12: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
?
Source: D. Lowe

## Slide 13: Practice with linear filters
0
0
0
1
0
0
0
0
0
Original
Shifted left
By 1 pixel
Source: D. Lowe

## Slide 14: Practice with linear filters
Original
?
1
1
1
1
1
1
1
1
1
Source: D. Lowe

## Slide 15: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
Blur (with a
box filter)
Source: D. Lowe

## Slide 16: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
?
(Note that filter sums to 1)
Source: D. Lowe

## Slide 17: Practice with linear filters
Original
1
1
1
1
1
1
1
1
1
0
0
0
0
2
0
0
0
0
-
Sharpening filter
  Accentuates differences with local average
Source: D. Lowe

## Slide 18: Sharpening
before
after
Slide credit: Bill Freeman

## Slide 19: Blurring the G component
R
G
B
original
processed
Slide credit: Bill Freeman

## Slide 20: Blurring the R component
original
processed
R
G
B
Slide credit: Bill Freeman

## Slide 21: Blurring the B component
original
R
G
B
processed
Slide credit: Bill Freeman

## Slide 22: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 23: Smoothing with box filter revisited
Smoothing with an average actually doesn’t compare at all well with a defocused lens
Most obvious difference is that a single point of light viewed in a defocused lens looks like a fuzzy blob; but the averaging process would give a little square
Source: D. Forsyth
Notes: I always walk through the argument on the left rather carefully; it gives some insight into the
significance of impulse responses or point spread functions.

## Slide 24: Smoothing with box filter revisited
Smoothing with an average actually doesn’t compare at all well with a defocused lens
Most obvious difference is that a single point of light viewed in a defocused lens looks like a fuzzy blob; but the averaging process would give a little square
Better idea: to eliminate edge effects, weight contribution of neighborhood pixels according to their closeness to the center, like so:
“fuzzy blob”
Source: D. Forsyth
Notes: I always walk through the argument on the left rather carefully; it gives some insight into the
significance of impulse responses or point spread functions.

## Slide 25: Gaussian Kernel
Constant factor at front makes volume sum to 1 (can be ignored, as we should re-normalize weights to sum to 1 in any case)
0.003 0.013 0.022 0.013 0.003
0.013 0.059 0.097 0.059 0.013
0.022 0.097 0.159 0.097 0.022
0.013 0.059 0.097 0.059 0.013
0.003 0.013 0.022 0.013 0.003
5 x 5,  = 1
Source: C. Rasmussen

## Slide 26: Choosing kernel width
Gaussian filters have infinite support, but discrete filters use finite kernels
Source: K. Grauman

## Slide 27: Choosing kernel width
Rule of thumb: set filter half-width to about 3 σ

## Slide 28: Example: Smoothing with a Gaussian

## Slide 29: Mean vs. Gaussian filtering

## Slide 30: Gaussian filters
Remove “high-frequency” components from the image (low-pass filter)
Convolution with self is another Gaussian
  So can smooth with small-width kernel, repeat, and get same result as larger-width kernel would have
  Convolving two times with Gaussian kernel of width σ is same as convolving once with kernel of width σ√2
Separable kernel
  Factors into product of two 1D Gaussians
Source: K. Grauman
Notes: Linear vs. quadratic in mask size

## Slide 31: Separability of the Gaussian filter
Source: D. Lowe

## Slide 32: Separability example
*
*
=
=
2D convolution (center location only)
Source: K. Grauman
The filter factors into a product of 1D filters:
Perform convolution along rows:
Followed by convolution along the remaining column:
For MN image, PQ filter: 2D takes MNPQ add/times, while 1D takes MN(P + Q)

## Slide 33: Overview of Filtering
Convolution
Gaussian filtering
Median filtering

## Slide 34: Alternative idea: Median filtering
A median filter operates over a window by selecting the median intensity in the window
Is median filtering linear?
Source: K. Grauman
Notes: Linearity of median filter: try filter([0 0 0; 0 1 0; 0 0 0] + [1 1 1; 1 1 2; 2 2 2])

## Slide 35: Median filter
Replace each pixel by the median over N pixels (5 pixels, for these examples). Generalizes to “rank order” filters.
5-pixel neighborhood
In:
Out:
In:
Out:
Spike noise is removed
Monotonic edges remain unchanged
Median([1 7 1 5 1]) = 1
Mean([1 7 1 5 1]) = 2.8

## Slide 36: Median filtering results
http://homepages.inf.ed.ac.uk/rbf/HIPR2/mean.htm#guidelines
Best for salt and pepper noise

## Slide 37: Median vs. Gaussian filtering
3x3
5x5
7x7
Gaussian
Median

## Slide 38: Derivative of Gaussian filter
Which one finds horizontal/vertical edges?
x-direction
y-direction

## Slide 39: Effect of  (Gaussian kernel spread/size)
Canny with
Canny with
original
The choice of  depends on desired behavior
  large  detects large scale edges
  small  detects fine features
Source: S. Seitz

## Slide 40: Scale of Gaussian derivative filter
Smoothed derivative removes noise, but blurs edge. Also finds edges at different “scales”.
1 pixel
3 pixels
7 pixels
Source: D. Forsyth